|

|

2

# Mounting and Wiring

Mount the sensor firmly so that the object to be detected is never within 51 mm (2.0 inches) of the face of the sensor.  For best results the sensor face should be parallel to the object surface.  Also the sensor should be away from air currents.

## Dimensions

## Wiring Connections

# Operation

When an object is detected inside the window limits, the black-wire NPN output is sinking, the white-wire PNP output is sourcing, and the amber LED is on.  When an object is not detected inside the window limits, the black-wire NPN output is non-sinking, the white-wire PNP is non-sourcing, and the amber LED is off.

This model sensor operates in the background mode, which means the sensor processes only the first object detected in the sensing range.  background mode is recommended for break-beam detector.  With object mode sensors, the sensor processes all echoes within the sensing range, and assumes the object is in the window if any echo is detected within the window.

## Multicolor LED States

The multicolor LED indicates the position of the object and not necessarily the state of the outputs if the delay times are not minimal.

|  | Multicolor Led | Object Position |
| --- | --- | --- |
|  | Off | Object not being detected |
|  | Red | Object detected outside the window limits |
|  | Green | Object detected inside the window limits |

## Amber LED

The amber LED shows the state of the outputs.  When the black-wire NPN output is sinking and the white-wire PNP output is sourcing, the amber LED is on.  When the black-wire NPN output is non-sinking and the white-wire PNP output is non-sourcing, the amber LED is off.

# Setting the Window Limits

Depress the setup pushbutton (the multicolor LED rapidly flashes amber to indicate the pushbutton is pressed) until the multicolor LED flashes green (about 3 seconds), and then release the setup pushbutton.  The multicolor LED continues flashing green indicating the sensor is waiting for the first limit.  Align a flat object parallel to the sensor face at the desired distance position for either window limit, and press the setup pushbutton once.  Upon release of the setup pushbutton, the multicolor LED flashes amber indicating the first limit is set and the sensor is waiting for the second limit.  Align a flat object parallel to the sensor face at the desired position for the second window limit and press the setup pushbutton once.  Upon release of the setup pushbutton, the multicolor LED turns to the color that indicates where the object is located.  The sensor has no timeout for setting limits.

To easily set the default window of 12.7 mm (0.50 in.), while the multicolor LED is flashing green requesting the first limit, align a flat object parallel to the sensor face at the center of the desired window, and press the setup pushbutton twice in succession.  This sets the limits 6.4 mm (0.25 in.) in front of and behind the object front surface.

While the setup pushbutton is depressed, the multicolor LED turns amber to indicate the sensor detects the object.  If the sensor does not detect the object, the multicolor LED is red while the setup pushbutton is depressed, and when the setup pushbutton is released after not detecting an object, the multicolor LED flashes red 2 seconds, and then requests that limit again by flashing green for the first limit or flashing amber for the second limit.

The limits are saved in nonvolatile memory and thus retained when power is removed from the sensor.

4

# Accessories

## Quick Connect Cables

Model: AC130	Straight, 4-conductor, 5 meters (16 feet)

Model: AC132	Right-angle, 4-conductor, 5 meters (16 feet)

5

## Mounting Brackets

MODEL AC233

.

# General Specifications

Power Supply:   +12 to 24 VDC @ 80 mA, excluding load

Sinking Output:

Maximum on-state voltage @ 100 mA: 0.37 volts

Maximum load current: 100 mA

Maximum applied voltage: 35 VDC

Protection:  ESD and over-current

Sourcing Output:

Maximum on-state voltage drop @ 100 mA: 1.0 volts

Maximum load current: 100 mA

Maximum output voltage: Equal to supply voltage

Protection:  ESD and over-current

Response Time:  20 milliseconds

Operating Temperature:

0(C to 50(C (32(F to 122(F) @ 100% relative humidity

Sensing:

Span:  51 to 991 mm (2.0 to 39.0 inches)

Limit Adjustment Resolution:  0.08 mm (0.003 inch)

Sensor Angle with respect to smooth flat surface:  90( ( 10(

Repeatability:   ( 0.86 mm (0.034 inch) from smooth flat surface at

constant air temperature

Quick Disconnect Cables (Optional):

AC130: Straight, 4-conductor, 5 meters (16 feet)

AC132: Right-angle, 4-conductor, 5 meters (16 feet)

Sensor Housing Material:

Case: PEI

Face: FDA approved silicone rubber

Sensor Ratings and Approvals

NEMA 4X (Indoor Use Only) 5, 12, 12K, 13, and IP67

Installation/Overvoltage Category: II

LIMITATIONS AND EXCLUSION OF WARRANTIES

All goods purchased from Hyde Park Electronics LLC shall be free from defects in materials, design and workmanship under normal conditions of use for one year from the date of shipment.  THIS WARRANTY IS THE SOLE WARRANTY AND IS EXPRESSLY IN LIEU OF ALL OTHER WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY IMPLIED WARRANTY OF MERCHANTABILITY OF FITNESS FOR A PARTICULAR PURPOSE.  THE LIABILITY OF HYDE PARK TO ANY PURCHASER SHALL BE LIMITED EXCLUSIVELY TO THE COST OF REPLACEMENT OR REPAIR OF DEFECTIVE PARTS, AND SHALL NOT INCLUDE LIABILITY FOR ANY DIRECT, CONSEQUENTIAL OR INCIDENTAL DAMAGES WHATSOEVER, WHETHER FORESEEN OR UNFORESEEN, INCLUDING BUT NOT LIMITED TO LOST PROFITS, LOST SALES, OR INJURY TO PERSONS OR PROPERTY.

This Product is UL Listed if powered by a Class II Power Supply and protected by a

2.0A Max UL Listed Fuse

HYDE PARK ELECTRONICS LLC

1875 Founders Drive

Dayton, Ohio  45420-4017

Phone (937) 252-2121   Fax (937) 258-5830

Email: help@sesensors.com

Web Site: http://www.sesensors.com

( 1997-2006 Hyde Park Electronics LLC

Ultrasonic Proximity Sensor

30 mm, No On/Off Delay

NPN & PNP Normally Open Outputs

SUPERPROX(

SM950A-100000

OPERATOR INSTRUCTIONS

This self-contained, ultrasonic proximity sensor provides both a NPN (sinking) and a PNP (sourcing) normally open (N.O.) output.  When an object is detected within the window, the black-wire NPN is sinking, the white-wire PNP is sourcing, and the amber LED is on.  When an object is not detected within the window, the NPN is non-sinking, the PNP is non-sourcing, and the amber LED is off.  Objects that are transparent, opaque, plastic, glass, metal, liquid, or solid can be detected within the sensing range. A multicolor LED indicates the zone of the object, and an amber LED is on when the outputs are active.

990.6 mm
(39.00 in.)

50.8 mm
(2.00 in.)

0.0 mm
(0.0 in.)

Figure 1

Literature and application engineering assistance are provided by

Hyde Park and its authorized distributors to aid the customer in selecting the product for an application.  The customer, however, is responsible for determining the suitability of the product in the application.

# Text boxes

U

N

I

N

T

E

N

D

E

D

O

P

E

R

A

T

I

O

N

Do not use this product to detect objects within the deadband.

Failure to follow this instruction can result in death, serious injury or

equipment damage.

W

A

RNING